﻿Specification Clauses

﻿Once the appropriate XPress product has been selected the use of one of the following specification clauses will provide the exact wording required to ensure that the correct product for the job is used.

XPress Copper fittings specification

"Press-fit fittings shall be of copper or copper alloy to the draft proposal Pr EN 1254 Part 7 and certified by WRAS and DVGW, capable of operating between –24°C and 110°C and rated 16 bar throughout the temperature range. Available in sizes from 15mm to 108mm they will be suitable for use with copper tube to BS EN 1057 R250/R290 on hot and cold water services, vented and unvented closed circuit heating, chilled water and low temperature hot water. They will provide electrical continuity, have a guarantee of 25 years against all manufacturing defects, and be drawn from the XPress Copper range manufactured by Yorkshire Fittings Limited".

XPress Copper System specification

"Press-fit fittings shall be of copper or copper alloy to the draft proposal Pr EN 1254 Part 7 and certified by WRAS and DVGW. Available in sizes from 15mm to 108mm they will be capable of operating between –24°C and 110°C and rated 16 bar throughout the temperature range. They will provide electrical continuity and be drawn from the XPress range from Yorkshire Fittings Limited. Copper tube shall be to BS EN 1057 R250/R290, be WRAS listed and drawn from the Yorkex range manufactured by Yorkshire Copper Tube Limited. The System when constructed exclusively from XPress Copper and Yorkex components will be suitable for use on hot and cold water services, vented and unvented closed circuit heating, chilled water and low temperature hot water and have a guarantee of 30 years against all manufacturing defects".

XPress Gas fittings specification

"Press-fit fittings shall be of copper or copper alloy to the draft proposal Pr EN 1254 Part 7 and approved to DVGW VP614 by the GWI and verified by Advantica for use with copper tube on 2nd and 3rd family gas service pipelines. Available in sizes from 15mm to 54mm they will be rated

5 bar for outside above ground use and 1 bar within buildings, capable of operating between –20°C and 70°C and tested to the requirements of HTC. The fittings will have a guarantee of 25 years against all manufacturing defects, and be drawn from the XPress Gas range manufactured by Yorkshire Fittings Limited".

XPress Gas System specification

"Press-fit fittings shall be of copper or copper alloy to the draft proposal Pr EN 1254 Part 7 and approved to DVGW VP614 by the GWI and verified by Advantica for use with copper tube on 2nd and 3rd family gas service pipelines. Available in sizes from 15mm to 54mm they will be rated

5 bar for outside above ground use and 1 bar within buildings, capable of operating between –20°C and 70°C and tested to the requirements of HTC. Copper tube shall be to BS EN 1057 R250/R290, and drawn from the Yorkex range manufactured by Yorkshire Copper Tube Limited.

The System when constructed exclusively from XPress Gas and Yorkex components will have a guarantee of 30 years against all manufacturing defects".

XPress Stainless fittings specification

"Press-fit fittings shall be of stainless steel material to

BS 316 S31/Din 1.4401 and certified by WRAS and DVGW, capable of operating between –20°C and 110°C and rated 16 bar throughout the temperature range. Available in sizes 15mm to 108mm they will be suitable for use with stainless steel 316 System tube from Yorkshire Fittings Limited or other stainless steel tube to BS 4127 or DVGW W541 on potable water services, general hot and cold water applications, heating, chilled water and low temperature hot water. They will provide electrical continuity, have a guarantee of 25 years against all manufacturing defects, and be drawn from the XPress Stainless range from Yorkshire Fittings Limited".

XPress Stainless System specification

"Press-fit fittings shall be of stainless steel material to

BS 316 S31/Din 1.4401 and certified by WRAS and DVGW. Available in sizes 15mm to 108mm they will be capable of operating between –20°C and 110°C and rated 16 bar throughout the temperature range. They will provide electrical continuity and be drawn from the XPress Stainless range manufactured by Yorkshire Fittings Limited. Stainless steel tube will be from

BS 316 S31/ Din 1.4401 stainless steel strip to BS 10088 Part 2 and be drawn from the stainless steel 316 System tube range from Yorkshire Fittings Limited. The System, when constructed exclusively from XPress Stainless fittings and stainless steel 316 System tube will be suitable for use on potable water services, general hot and cold water applications, heating, chilled water and low temperature hot water, and have a guarantee of 30 years against all manufacturing defects".

XPress Carbon fittings specification

"Press-fit fittings shall be of carbon steel in sizes from 15mm to 108mm, they will be capable of operating between –20°C and 110°C and rated 16 bar throughout the temperature range. Suitable for use on vented and unvented closed circuit heating and chilled water applications, with galvanised or plastic coated carbon steel System tube to DIN 2394/NEN 1982 or other carbon steel tube to

DIN 2394/NEN 1982. They will provide electrical continuity, have a guarantee of 5 years against all manufacturing defects and be drawn from the XPress Carbon range from Yorkshire Fittings Limited".

XPress Carbon System specification

"Press-fit fittings shall be of carbon steel in sizes from 15mm to 108mm, they will be capable of operating between –20°C and 110°C and rated 16 bar throughout the temperature range.

They will provide electrical continuity and be drawn from the XPress Carbon range from Yorkshire Fittings Limited. Tubes shall be galvanised/plastic coated carbon steel System tube to

DIN 2394/NEN 1982 drawn from the XPress Carbon range from Yorkshire Fittings Limited. The system will be constructed exclusively from XPress Carbon components, will be suitable for use on vented and unvented closed circuit heating and chilled water applications and have a guarantee of 10 years against all manufacturing defects".